## Slide 1: Basic Organization of a Computer System Chapter 2

## Slide 2: Bits and Bytes
A bit is a binary digit, the smallest increment of data on a computer.
A bit can hold only one of two values: 0 or 1, corresponding to the electrical values of off or on, respectively.
Because bits are so small, you rarely work with information one bit at a time.
Bits are usually assembled into a group of eight to form a byte.
A byte contains enough information to store a single ASCII character, like "h".

## Slide 3: Bits and Bytes
So in computer jargon, the following units are used:
Unit | Equivalent
1 kilobyte (KB) | 1,024 bytes
1 megabyte (MB) | 1,048,576 bytes
1 gigabyte (GB) | 1,073,741,824 bytes
1 terabyte (TB) | 1,099,511,627,776 bytes
1 petabyte (PB) | 1,125,899,906,842,624 bytes

## Slide 4: Basic Organization of a Computer System
The basic organization of a computer system is the processing unit, memory unit, and input-output devices. The processing unit controls all the functions of the computer system.
It is the brain of the computer e.g. CPU.
The memory unit consists of two units. One is an arithmetic unit and the other is a logic unit.
Input devices are those devices through which end-users can send messages to computers e.g. keyboard, mouse, etc.
Output devices are those devices through which end-users get output from computers e.g. monitors.

## Slide 5: Remember IPOS Cycle?
Control Unit
Arithmetic/Logical Unit
Memory Unit
Central Processing Unit (CPU)
Input
Output
Storage

## Slide 6: Central Processing Unit (CPU)
  A CPU is a brain of a computer. It is responsible for all functions and processes.
  Carries out instructions from the program & Manipulate the data
The actual processing of the data is carried out in the CPU.
The CPU stores the data and instructions in the primary memory of the computer, called the Random Access Memory (RAM) and processes them from this location.

## Slide 7: Central Processing Unit (CPU)
The Arithmetic Logic Unit (ALU) and the Control Unit (CU) are the two subcomponents of the CPU.
The ALU carries out the arithmetic and logical operations while the CU retrieves the information from the storage unit and interprets this information.
The CPU also consists of circuitry devices called cache and registers.
Notes: Jawad 16
Hareem 23

## Slide 8: Arithmetic Logic Unit (ALU)
Executes all arithmetic and logical operations.
Arithmetic calculations like as addition, subtraction, multiplication and division.
Logical operation like compare numbers, letters, or special characters.
The data and instructions stored in the RAM are transferred to the ALU for processing. The ALU performs the logical and the arithmetic operations on the data and the results are temporarily stored in the RAM. After the processing, the final results are stored in the secondary memory, i.e., the storage unit, and are released through an output device.

## Slide 9: Control Unit (CU)
Controls and co-ordinates computer components.
Read the code for the next instruction to be executed.
Increment the program counter so it points to the next instruction.
Read whatever data the instruction requires from cells in memory.
Provide the necessary data to an ALU or register.
If the instruction requires an ALU or specialized hardware to complete, CU instructs the hardware to perform the requested operation.
It selects, interprets, and ensures the proper execution of the program instructions.

## Slide 10: Registers
To speed up the Computer processor's work by enabling quick access to often-used values, it has a collection of Registers that are incredibly fast but only hold a small quantity of data.
Computer registers are memory storing units that operate at high speed. It's a component of a computer's processor. It can hold any type of data, including a bit sequence or a single piece of data.
Eight registers, a memory unit, and a control unit make up a basic computer. These devices must be connected on a regular basis.

## Slide 11: Types of Registers
Most common registers in computer:
Accumulator (processor register)
Program Counter (stores address of instructions)
Address Register (stores memory addresses)
Data Register (general purpose register used for storing data during calculations)
Instruction Register (stores current instructions being executed)
Temporary Register (holds the temporary data)

## Slide 12: Characteristics of Registers
Small, storage locations within the CPU
Manipulated directly by the Control Unit
Wired for specific function
Size in bits or bytes (not MB like memory)
Can hold data, an address or an instruction
The more registers a CPU has available, the faster it can work

## Slide 13: Functions of Registers in Computer Architecture
Data Storage: Registers are used for the temporary storage of data or instructions during the execution of the program. They are mainly used to store information for a small time so that the CPU can access it quickly.
Data Processing: We can perform various logical and arithmetic operations with the help of a register and the data of these instructions is stored in the accumulator register.
Addressing: Registers are used to store memory addresses they can store the address of the instruction or the data that the CPU wants to access either to read from or write to.
Data Transfer: Registers are used to transfer data between CPU and memory. Some of them hold the data that is read from or written to memory.
Control: We can control the order of execution of instructions as some registers temporarily store the current instruction being processed, while others hold the next instruction to be executed.

## Slide 14: Microprocessor
A microprocessor is an integrated circuit (IC) which incorporates core functions of a computer's central processing unit (CPU).
It is a programmable multipurpose silicon chip, clock driven, register based, accepts binary data as input and provides output after processing it as per the instructions stored in the memory.
Cache:
A cache is a smaller, high-speed volatile memory located between the CPU (Central Processing Unit) and the main memory (RAM) in a computer system. Its primary function is to store copies of frequently accessed or recently used data and instructions temporarily, allowing the CPU to access them quickly when needed.

## Slide 15: Microprocessor
A microprocessor executes a collection of machine instructions that tell the processor what to do. Based on the instructions, a microprocessor does three basic things:
  Using its ALU (Arithmetic/Logic Unit), a microprocessor can perform mathematical operations like addition, subtraction, multiplication and division. OR CU for data management
  A microprocessor can move data from one memory location to another.
  A microprocessor can make decisions and jump to a new set of instructions based on those decisions.

## Slide 16: Bus
Alternatively known as an address bus, data bus, control bus, or local bus, a bus is a link between components or devices connected to a computer. This expression covers all related hardware components (wire, optical fiber, RAM sticks slot etc.)
For example, a bus carries data between a CPU and the system memory via the motherboard.
You can think of a computer bus like public transportation or a school bus. These types of buses are capable of transporting people from one destination to another destination. Like these buses, a computer bus transmits data from one location or device to another location or device.

## Slide 17: Types of Computer Buses
A bus is either a parallel or serial bus, and either an internal bus (local bus) or an external bus (expansion bus).
Internal bus vs. External bus
An internal bus enables the communication between internal components, such as a video card and memory.
An external bus can communicate with external peripherals, such as a USB.
Parallel bus vs. Serial bus
A computer bus can transmit its data using either a parallel or serial method of communication.
With a parallel bus, data is transmitted several bits at a time. However, with a serial bus, the data is transferred one bit at a time.