## Slide 1: Introduction to Number Systems

## Slide 2: Non-Positional Number System
A non-positional number system uses a limited number of symbols in which each symbol has a value.
However the position a symbol occupies in the number normally bears no relation to its value.
The value of each symbol is fixed.

## Slide 3: Non-Positional Number System
Roman number system is an example of a non-positional number system.
This number system has a set of symbols.
S={I, V, X, L, C, D, M}.
Values of symbols in the Roman number system.
Symbol I V X L C D M
Value 1 5 10 50 100 500 1000

## Slide 4: Positional Number System
A positional (numeral) system is a system for representation of numbers by an ordered set of numerals symbols (called digits) in which the value of a numeral symbol depends on its position.
For each position a unique symbol or a limited set of symbols is used.

## Slide 5: Positional Number System
Each symbol represents different value depending on the position they occupy in a number.
The value of a symbol is given by the weight of its position expressed in the bases (or radices) of the system.

## Slide 6: Positional Number System – Terminologies

## Slide 7: Decimal Number System
The decimal number system is an example of positional number system because the value of the number depends on the position of the digits.
For example, the number 12345 has a very different value than the number 54321, although the same digits are used in both numbers.

## Slide 8: Decimal Number System
Ten Digits: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 – Base 10
Example:
Digit is the least significant digit (LSD)
Digit is the most significant digit (MSD)

## Slide 9: Binary Number System
Two Digits: 0, 1 – Base 2
Example:
Digit is the least significant bit (LSB)
Digit is the most significant bit (MSB)

## Slide 10: Base-N Number System
N Digits: 0, 1, 2, 3, 4, 5, …, N-1 – Base N
Example:
Digit is the least significant digit (LSD)
Digit is the most significant digit (MSD)

## Slide 11: Number Systems
Four number system
        Decimal (10)
        Binary (2)
        Octal (8)
        Hexadecimal (16)
        ............

## Slide 12: Binary numbers?
Computers work only on two states
  On
  Off
Basic memory elements hold only two states
  Zero / One
Thus a number system with two elements {0,1}
A binary digit – bit !

## Slide 13: Decimal numbers
1439 = 1 x 103 + 4 x 102 + 3 x 101 + 9 x 100
      Thousands Hundreds Tens Ones
Radix = 10

## Slide 14: Binary Decimal
1101 = 1 x 23 + 1 x 22 + 0 x 21 + 1 x 20
= 1 x 8 + 1 x 4 + 0 x 2 + 1 x 1
= 8 + 4 + 0 + 1
(1101)2 = (13)10
1, 2, 4, 8, 16, 32, 64, 128, 256, 512, ….

## Slide 15: Decimal Binary
13
6
3
1
0
2
2
2
2
1
0
1
1
(13)10 = (1101)2
MSB
LSB

## Slide 16: Octal Decimal
137 = 1 x 82 + 3 x 81 + 7 x 80
= 1 x 64 + 3 x 8 + 7 x 1
= 64 + 24 + 7
(137)8 = (95)10
Digits used in Octal number system – 0 to 7 so 108 will not be part of it as 8 is out of range.

## Slide 17: Decimal Octal
95
11
1
0
8
8
8
7
3
1
(95)10 = (137)8
MSP
LSP

## Slide 18: Hex Decimal
BAD = 11 x 162 + 10 x 161 + 13 x 160
= 11 x 256 + 10 x 16 + 13 x 1
= 2816 + 160 + 13
(BAD)16 = (2989)10
A = 10, B = 11, C = 12, D = 13, E = 14, F = 15

## Slide 19: Decimal Hex
2989
186
11
0
16
16
16
13
10
11
(2989)10 = (BAD)16
MSP
LSP

## Slide 20: Why octal or hex?
Ease of use and conversion
Three bits make one octal digit
111 010 110 101
7 2 6 5 => 7265 in octal
Four bits make one hexadecimal digit
1110 1011 0101
E B 5 => EB5 in hex
4 bits = nibble

## Slide 22: Negative numbers
Three representations
      Signed magnitude
      1’s complement
      2’s complement

## Slide 23: Sign magnitude
Make MSB represent sign
Positive = 0
Negative = 1
E.g. for a 3 bit set
  “-2”
Sign | Bit | Bit
1 | 1 | 0
MSB |  | LSB

## Slide 24: 1’s complement
MSB as in sign magnitude
Complement all the other bits
Given a positive number complement all bits to get negative equivalent
E.g. for a 3 bit set
  “-2”
Sign | Bit | Bit
1 | 0 | 1
0 | 1 | 0

## Slide 25: 2’s complement
1’s complement plus one
E.g. for a 3 bit set
  “-2”
Sign | Bit | Bit
1 | 1 | 0
0 | 1 | 0

## Slide 26
Decimal number | Signed magnitude | 2’s complement | 1’s complement
3 | 011 | 011 | 011
2 | 010 | 010 | 010
1 | 001 | 001 | 001
0 | 000 | 000 | 000
-0 | 100 | --- | 111
-1 | 101 | 111 | 110
-2 | 110 | 110 | 101
-3 | 111 | 101 | 100
-4 |  | 100 | 
No matter which scheme is used we get an even set of numbers but we need one less (odd: as we have a unique zero)

## Slide 27: Binary Arithmetic
Addition / subtraction
Unsigned
Signed
  Using negative numbers

## Slide 28: Unsigned: Addition
Like normal decimal addition
B
A
The carry out of the MSB is neglected
+ | 0 | 1
0 | 0 | 1
1 | 1 | 10
0101 (5)
+ 1001 (9)
1110 (14)

## Slide 29: Unsigned: Subtraction
Like normal decimal subtraction
B
A
A borrow (shown in red) from the MSB implies a negative
- | 0 | 1
0 | 0 | 11
1 | 1 | 0
1001 (9)
- 0101 (5)
0100 (4)

## Slide 30: Signed arithmetic
Use a negative number representation scheme
Reduces subtraction to addition

## Slide 31: 2’s complement
Negative numbers in 2’s complement
001 ( 1)10
101 (-3)10
110 (-2)10
The carry out of the MSB is lost

## Slide 32: Overflow / Underflow
Maximum value N bits can hold : 2n –1
When addition result is bigger than the biggest number of bits can hold.
  Overflow
When addition result is smaller than the smallest number the bits can hold.
  Underflow
Addition of a positive and a negative number cannot give an overflow or underflow.

## Slide 33: Overflow example
011 (+3)10
011 (+3)10
110 (+6)10 ????
1’s complement computer interprets it as –1 !!
(+6)10 = (0110)2 requires four bits !

## Slide 34: Underflow examples
Two’s complement addition
101 (-3)10
101 (-3)10
Carry 1 010 (-6)10 ????
The computer sees it as +2.
(-6)10 = (1010)2 again requires four bits !